## Slide 1
PULSE-LEAD PEAK DETECTION
PULSE-LEAD PEAK DETECTION
USEN

## Slide 2
For what kind of problem
INTRODUCTION
01
Innovation approach for the goal
METHODOLOGY
02
Performance of model detection
RESULT
03
Future improvement of this method
PROSPECT
04

## Slide 3
Introduction
Motivation
Finding peaks is simple, but which of them are caused by pulse?
If we can eliminate the peaks caused by noise, much valuable information can be gained

## Slide 4
Introduction
Recurrence Plot (RP)
Signal
Recurrence Plot
When time=15 & time=25, signal have the same signal value. This is called a recurrence.
Then on recurrence plot, asset black points on (15 , 25) and (25 , 15)
In punctilious definition, a recurrence does not require exactly same signal value, being similar is also regarded as a recurrence

## Slide 5
Introduction
Despite the tedious definition, a RP can be draw by implement the logic matrix below
Example of RP based on PPG signal
Recurrence Plot
||A - B|| : Euclidean distance between A and B

## Slide 6
Introduction
Systolic Peak
Diastolic Peak
End of one pulse wave
Crossbow
The “crossbow” from RP indicates the information of one pulse wave

## Slide 7
Flowsheet of the Project
Overview
RP
Training Data
Label
CNN Training
Algorithm
Predictive Model
Testing Data
RP
Label
Estimation
Comparison
Noise-added Training Data
Noise-added Testing Data
Algorithm 0
Algorithm 0
Algorithm 1
Algorithm 2
Algorithm 1
Algorithm 2
Methodology

## Slide 8
Methodology
Adding Noise into Data
Algorithm 0
Goal is adding fake peaks into signal
Eventually the noise level can be controlled by 2 parameters
  Frequency of Noise
  Amplitude of Noise
higher amplitude
higher frequency

## Slide 9
Methodology
From Signal to RP
Algorithm 1
Form A
Form B
Recurrence plot has 2 different forms.
  Form A: composed by 0&1, only contains black points and white blank
  Form B: composed by absolute distance, exists as grayscale image

## Slide 10
Methodology
A. Naïve Method
Algorithm 2
Step 1: record precise peak position
  Peak Truth is a binary array in the form of [0,0,0,1,0,0,0,0,1,0,…] (lack of information)
Data
signal value
Peak Truth
is peak or not
Label
probability of being a peak
Step 2: assign weights to points near the peak
  Label provides information on the region where the peak is located.

## Slide 11
Methodology
B. Statistical Method
Algorithm 2
Step 1: Use a sliding window to calculate a dynamic threshold
Selected points are peak-related points
Based on statistical hypothesis testing, points above the threshold have high chance to be a peak point
Step 2: Normalize peak-related regions
Squeeze values into [0,1] by cumulative density function of normal distribution
Label
probability of being a peak
Peak-related Regions
points above threshold
Data
signal value

## Slide 12
Methodology
Naïve vs Statistical
Algorithm 2
Statistical method is well-supported by theories. And it takes the width of pulse wave into considerration
But statistical method still requires future improvements since sometimes it mix up diastolic peak & systolic peak

## Slide 13
Result
Distance Error: the distance between real peak and estimated peak
Use the Mean Distance Error with better interpretation: average accuracy of estimated peak
Error Rate: the percentage of model incorrectly predict the number of peaks
Evaluation Standard

## Slide 14
Result
Feasibility Test
Noise Level: Amplitude=3.5 Frequency=1.3 (Median Level)
Mean Distance Error = 0.23
Error Rate = 1/500

## Slide 15
Result
Grid Search
Noise level can be controlled by 2 parameters
  Frequency of Noise
  Amplitude of Noise
higher amplitude
higher frequency
Try different combinations within the reasonable range and check model performance
Data scale:
  Sample size = 5000
  Testing : Training : Validation = 8:1:1
  Sampling rate = 60
  Signal duration = 5s

## Slide 16
Result
Grid Search

## Slide 17
Low Frequency & Low Amplitude

## Slide 18
High Frequency & Low Amplitude

## Slide 19
Low Frequency & High Amplitude

## Slide 20
High Frequency & High Amplitude

## Slide 21
Result
Grid Search
Rate is too low, so just use the cumulative sum of wrong estimation count

## Slide 22
PROSPECT
Summary
RP
Training Data
Label
CNN Training
Algorithm
Predictive Model
Testing Data
RP
Label
Estimation
Comparison
Noise-added Training Data
Noise-added Testing Data
Algorithm 0
Algorithm 0
Algorithm 1
Algorithm 2
Algorithm 1
Algorithm 2

## Slide 23
PROSPECT
Future Improvement
Limitation of synthetic data and synthetic noise.
Implementation of statistical method for labeling method
More elaborate model architecture
Fitness for higher dimensional data(RGB signal)
RP
Training Data
Label
CNN Training
Algorithm
Predictive Model
Testing Data
RP
Label
Estimation
Comparison
Noise-added Training Data
Noise-added Testing Data
Algorithm 0
Algorithm 0
Algorithm 1
Algorithm 2
Algorithm 1
Algorithm 2

## Slide 24
- THANK YOU -